## Slide 1: Embrace deliverable D2.1 CRML specification v1.0
Daniel Bouskela
EDF Lab
Chatou, France
CRML Design Group
Jan. 15, 2021
EMBrACE

## Slide 2: Introduction

## Slide 3: Language architecture
CRML
Temporal logic
Simulation
Model checking
High level constructs
Objects, sets and classes
Behavior
State machines
Test sequences
ETL

## Slide 4: Mathematical foundations

## Slide 5: Definition of requirements, time periods and events
R := (true | false | undecided | undefined | ϕ)P
P := ([ | ]) opening_event, closing_event ([ | ])
event := R [+ duration ]
A requirement is a condition ϕ associated with a time period P. A condition is a 2-, 3- or 4-valued Boolean. The value of a requirement is a 4-valued Boolean. A requirement is a function of time.
A time period is a time interval between two events. The left and right boundaries can be included or excluded.
An event corresponds to a single occurrence of a 2-, 3- or 4-valued Boolean becoming true.
The condition ϕ associated with R is denoted R: R := ϕ. The time period P associated with R is denoted R: R := P.

## Slide 6: Definition of the 4-valued logical operators
ϕ := ϕ | ¬ϕ | ϕ1 ᴧ ϕ2
Conditions and requirement values satisfy a 4-valued Boolean algebra.
The negation (¬) and conjunction (ᴧ) logical operators are defined with truth tables.
and | Logical conjunction |  |  | 
ϕ1 ᴧ ϕ2 | true | false | undecided | undefined
true | true | false | undecided | true
false | false | false | false | false
undecided | undecided | false | undecided | undecided
undefined | true | false | undecided | undefined
not | Logical negation |  |  | 
ϕ | true | false | undecided | undefined
¬ϕ | false | true | undecided | undefined
ϕ1 and ϕ2 represent the values of two different variables at the same instant in time
ϕ1
ϕ2

## Slide 7: Definition of the 4-valued logical operators
All other logical operators are defined with the Morgan laws.
  Logical disjunction
ϕ1 ᴠ ϕ2 := ¬(¬ϕ1 ᴧ ¬ϕ2)
  Logical exclusive disjunction
ϕ1  ϕ2 := (ϕ1 ᴠ ϕ2) ᴧ ¬(ϕ1 ᴧ ϕ2)
  Logical inference
ϕ1  ϕ2 := ¬ ϕ1 ᴠ ϕ2

## Slide 8: 4-valued logical Equality operator
The equality of Boolean ϕ1 with Boolean ϕ2 when event E occurs is
E
ϕ1
ϕ2
(ϕ1 = ϕ2)E :=
for t  [ E, E ]
true if ϕ1(t)  ϕ2(t)
false if ϕ1(t)  ϕ2(t)
for t  [ E, E ]
undefined
(ϕ1 = ϕ2)E

## Slide 9: Examples
  R1 = a]b, c] (a,b,c: Boolean, c = ¬c)
  R2 = ….
  R3 = (¬R1 ᴧ R2)[R1, R1 + 10 s]
  R4 = (R2 ᴠ R3)P1
  R5 = R4P2

## Slide 10: Definition of the 4-valued temporal operators
Previous operator
 ϕ(t) := ϕ(t  dt) for the continuous clock
 ϕ(ti) := ϕ(ti1) for a discrete clock
ϕ := ϕ |  ϕ | d ϕ | ϕ1 x ϕ2 | ϕ1 – ϕ2 | ϕ1 + ϕ2
d ϕ := ϕ   ϕ
Differential operator

## Slide 11: Definition of the 4-valued temporal operators
a x ϕ :=
undecided iff a = false
ϕ iff a = true
Filter operator
a and ϕ represent resp. the values of a 2-valued and a 4-valued Boolean variable at different instants in time
a
ϕ
ϕ := ϕ |  ϕ | d ϕ | ϕ1 x ϕ2 | ϕ1 – ϕ2 | ϕ1 + ϕ2
x | Filter |  |  | 
a x ϕ | true | false | undecided | undefined
true | true | false | undecided | undefined
false | undecided | undecided | undecided | undefined

## Slide 12: Definition of the 4-valued temporal operators
Difference operator
ϕ1 and ϕ2 represent the values of the same variable at different instants in time
ϕ1
ϕ2
ϕ := ϕ |  ϕ | d ϕ | ϕ1 x ϕ2 | ϕ1 – ϕ2 | ϕ1 + ϕ2
– | Detects events |  |  | 
ϕ2 – ϕ1 | true | false | undecided | undefined
true | undecided | true | undecided | true
false | false | undecided | undecided | false
undecided | undecided | undecided | undecided | undecided
undefined | true | false | undecided | undefined

## Slide 13: Definition of the 4-valued temporal operators
Addition operator
ϕ1 and ϕ2 represent the values of the same variable at different instants in time
ϕ1
ϕ2
+ | Accumulates events |  |  | 
ϕ1 + ϕ2 | true | false | undecided | undefined
true | true | false | true | true
false | false | false | false | false
undecided | true | false | undecided | undecided
undefined | true | false | undecided | undefined
ϕ := ϕ |  ϕ | d ϕ | ϕ1 x ϕ2 | ϕ1 – ϕ2 | ϕ1 + ϕ2

## Slide 14: Definition of the 4-valued temporal operators
Integral operator
ϕ := ϕ |  ϕ | d ϕ | ϕ1 x ϕ2 | ϕ1 – ϕ2 | ϕ1 + ϕ2
ϕ() d := ϕ() x d

 P

P
ϕ :=

ϕP

tiP
ϕ(ti) := ϕ(t1) + ϕ(t2) + … ϕ(ti) + …
Sum operator
with ti covering all time instants within P

## Slide 15: Definition of the Value of a requirement
The value of requirement R = ϕP is the Boolean
Therefore, the val function goes from the domain of requirements to the domain of Booleans
where is the domain of requirements and is the domain of time periods.
a(ϕ) depends on the condition ϕ. It filters out the events dϕ that are not decision events.
Examples:
ϕ := count (E, P)  2
a(ϕ) := count (E, P)  2 = ¬ϕ
ϕ := count (E, P)  3
a(ϕ) := count (E, P)  3 = ϕ
val(R) := a(ϕ) dϕ

ϕ P
val: 

## Slide 16: Events generated by requirements
An event R generated by requirement R is defined as
R := val(R)

## Slide 17: Definition of the satisfaction of a requirement
P1 ╞ ϕ1 ᴧ P2 ╞ ϕ2 := val(ϕ1P1) ᴧ val(ϕ2P2) = true
¬(P ╞ ϕ) := ¬val(ϕP) = true
P1 ╞ ϕ1 ᴠ P2 ╞ ϕ2 := ¬(¬P1 ╞ ϕ1 ᴧ ¬P2 ╞ ϕ2)
P1 ╞ ϕ1  P2 ╞ ϕ2 := ¬P1 ╞ ϕ1 ᴠ P2 ╞ ϕ2
P1 ╞ ϕ1  P2 ╞ ϕ2 := (P1 ╞ ϕ1 ᴠ P2 ╞ ϕ2) ᴧ ¬(P1 ╞ ϕ1 ᴧ P2 ╞ ϕ2)
Requirement R = ϕP is satisfied iff val(R) = true
The satisfaction of requirements composed with logical operators is given by
P╞ ϕ := val(R) = true

## Slide 18: Logical operations on requirements
As
Logical operations on requirements can be defined as follows:
P1 ╞ ϕ1 ᴧ P2 ╞ ϕ2 := val(ϕ1P1) ᴧ val(ϕ2P2) = true
¬(P ╞ ϕ) := ¬val(ϕP) = true
R1 ᴧ R2 := val(R1) ᴧ val(R2)
¬R := ¬val(R)
R1 ᴠ R2 := ¬(¬R1 ᴧ ¬R2)
R1  R2 := ¬R1 ᴠ R2
R1  R2 := (R1 ᴠ R2) ᴧ ¬(R1 ᴧ R2)

## Slide 19: Definition of The continuous clock
There is one continuous clock denoted . It represents the Newtonian time. All time instants t  .
All time instants t in have a value which depends on an arbitrary time origin t0. Therefore, only time differences (or delays) t2  t1 are meaningful.
Events always occur in the continuous time domain.
If R1 occurs at time t1, and R2 occurs at time t2, then the delay between the two events is given by R2  R1. There is no need to get the values of t1 and t2 which are meaningless. The time difference is given by t2  t1 = R2  R1.

## Slide 20: Functions of events
Many functions take events as arguments. Example: delay(R2, R1) = R2  R1
Let f(R) be a function that takes event R as argument.
Although R occurs at time instants when R becomes true, f is defined for any time instant t  as follows: the value of f(R) at instant t is equal to the value of f(R) at instant ti where ti is the instant of the last occurrence of R. Before the first occurrence of R, the value of f(R) is undefined.
The definition is similar for functions f taking several events as arguments: the value of f is undefined before the first occurrence of all the events in arguments, and does not change between events.
(R) 
R  f(R)
(R)
f(R)
t0
ti
ti+1
ti1

## Slide 21: Operations on Booleans in the continuous clock domain
duration
duration
R + duration
R
R
R+ duration
R
R + duration
R = ¬R
Delay: R := R + duration
(R + duration)(t) := R(t  duration)
The value of duration is taken at the instant of occurrence of R: duration := duration(R)

## Slide 22: Operations on Booleans in the continuous clock domain
The duration of a Boolean ϕ over a time period P is the elapsed time ϕ is true inside P
int is the function
duration (ϕ, P) := int(ϕ) dt

t P
int(ϕ) :=
1 if ϕ = true
0 if ϕ  true

## Slide 23: Operations on events in the continuous clock domain
Delay: R2 := R1 + duration with duration 
duration
duration
R + duration
R
R
R+ duration
R
R + duration
R = ¬R
R + duration := (R + duration)
duration = (R + duration)  R
The value of duration is taken at the instant of occurrence of R: duration := duration(R)
Elapsed time: duration := R2  R1 with duration 

## Slide 24: Operations on events in the continuous clock domain
First: R1  R2
Definition using clocks:
R1
R2
R1  R2 :=
R1 if R1 occurs before R2
R2 if R2 occurs before R1
R1  R2
R1  R2 := (R1 R2)( == 1)

## Slide 25: Operations on events in the continuous clock domain
Strictly before: R1  R2.
The value of R1  R2 is decided at time instants when R1 or R2 have occurred. If R1 and R2 have occurred, then R1  R2 = R2  R1  0
R1
R2
R1  R2 undecided
R1  R2 true or false
R1  R2 = R2  R1  0
R1 R2 :=
for t  [ R1 R2, +  [
true if R1 occurs strictly before R2
false otherwise
for t  [ - , R1 R2 [
undecided

## Slide 26: Operations on events in the continuous clock domain
Before: R1  R2.
The value of R1  R2 is decided at time instants when R1 or R2 have occurred. If R1 and R2 have occurred, then R1  R2 = R2  R1  0
R1
R2
R1  R2 undecided
R1  R2 true or false
R1  R2 = R2  R1  0
R1  R2 :=
for t  [ R1 R2, +  [
true if R1 occurs before R2
false otherwise
for t  [ - , R1 R2 [
undecided

## Slide 27: Operations on events in the continuous clock domain
Strictly after: R1  R2.
The value of R1  R2 is decided at time instants when R1 or R2 have occurred. If R1 and R2 have occurred, then R1  R2 = R1  R2  0
R1
R2
R1  R2 undecided
R1  R2 true or false
R1  R2 = R1  R2  0
R1  R2 :=
for t  [ R1 R2, +  [
true if R1 occurs strictly after R2
false otherwise
for t  [ - , R1 R2 [
undecided

## Slide 28: Operations on events in the continuous clock domain
After: R1  R2.
The value of R1  R2 is decided at time instants when R1 or R2 have occurred. If R1 and R2 have occurred, then R1  R2 = R1  R2  0
R1
R2
R1  R2 undecided
R1  R2 true or false
R1  R2 = R1  R2  0
R1  R2 :=
for t  [ R1 R2, +  [
true if R1 occurs after R2
false otherwise
for t  [ - , R1 R2 [
undecided

## Slide 29: Opening and closing events of a time period
P := ([ | ]) opening_event, closing_event ([ | ])
The opening event is denoted P.
The closing event is denoted P.
Therefore P := ([ | ]) P, P ([ | ]).
P
P
P

## Slide 30: Events Inside a time period
Event E occurring inside time period P is denoted E  P.
E  P := E  P and E  P.
 and  must be replaced by  and  if boundaries are not included.
P
P
P
E

## Slide 31: Operations on Booleans in the continuous clock domain
trim (R, P) :=
ϕ =

ϕP

trim (ϕ, P)

## Slide 32: Definition of Discrete Clocks
A discrete clock tick is an occurrence of an event E. The discrete clock domain is denoted .
A discrete clock is a set of ticks ordered in time. A clock can have a predefined or non-predefined number of ticks.
Clocks generated by the same Boolean R are denoted
Time associated to a discrete clock is given by the sequence number of the clock tick, but each clock tick is associated with its time occurrence in the continuous clock domain. The ith tick of clock  is denoted i = R(ti). It is occurring at time i  in the discrete clock domain and at time ti  in the continuous clock domain.
R
R
R
R
 = { E1, E2, …, Ei, … }
(R) = { R(t1), R(t2), … }

## Slide 33: Operations on events in a discrete clock domain
Projection: R/dt is the first tick E of clock  following R if E  R < dt with dt 
R/ := R/dt=0. The ticks of  are all occurrences of R/.
E
E
E
E
R
(E)
R/dt
dt

## Slide 34: Operations on events in a discrete clock domain
Delay: R2/ := R1/ + n with n. R2/ occurs n ticks after R1/ occurs.
Elapsed time: duration := R2/  R1/ with duration 
The value of duration is taken at the instant of occurrence of R/ : duration := duration(R/)
duration = 3
R
R+ duration
(R)

## Slide 35: Operations on discrete clocks
Clock delay: (R) + duration := (R + duration)
Clock union: (R1) ᴠ (R2) := (R1 ᴠ R2)
duration
(R)
(R) + duration
(R1)
(R2)
(R1 ᴠ R2)

## Slide 36: Operations on discrete clocks
Clock projection on another clock: (R1) / (R2) := { i(R1) / (R2), i  }
Clock transformation into a multiple time period: ((R)) := ([ R, R ])
(R1)
(R2)
(R1) / (R2)
(R)
((R))

## Slide 37: Operations on discrete clocks
Tick filter: (cond ) := { i, cond(i) = true } cond: condition
(R)
(R)(  2)
(R)(3    6)
(R)(  4)
(R)(  1 mod 3)
(R)(  0 mod 2)
(R1)
(R2)
(R1) / (((R2)(  1 mod 2))

## Slide 38: Operations on discrete clocks
Clock tick counter on time period P: count ((R), P) := card((  P))
(R)
P
P
P

## Slide 39: Operations on discrete clocks
Converting a clock to a Boolean: R’ = (R))
false
true
(R)
(R))

## Slide 40: Operations on Events and clocks
Union of two events: (E1 ᴠ E2) := { E1, E2 }
Union of a clock with an event: (R) ᴠ E = E ᴠ (R) := (R)  { E }
E1
E2
E1
E2
(E1 ᴠ E2)
(R) ᴠ E
E
(R)
E

## Slide 41: Definition of MULTIPLE time periods
R1
R1
R1
R2
P1
P2
P3
R2
A multiple time period is a set of time periods ordered by increasing opening events
P1 // P2 // … // Pn := { P1, P2, …, Pn }
(([ | ]) R1, R2 ([ | ]) := //R1, R2 ([ | ]) R1, R2 ([ | ])
Multiple time periods opened at all occurrences of R1 and closed at all occurrences of R2 are denoted

## Slide 42: Definition of MULTIPLE time periods in the continuous clock domain
Multiple time periods for which a given time period open at R is closed at occurrence of R + duration are denoted
(([ | ]) R, duration ([ | ]) := //R ([ | ]) R, R + duration ([ | ])
R
R
R
P1
P2
P3
duration
duration
duration
The value of duration is taken at the instant of occurrence of R: duration := duration(R).
duration 

## Slide 43: Definition of MULTIPLE time periods in A discrete clock domain
Multiple time periods for which a given time period open at R is closed at occurrence of R + duration in the discrete clock domain  are denoted
(([ | ]) R/, duration ([ | ]) := //R ([ | ]) R/, R/ + duration ([ | ])
The value of duration is taken at the instant of occurrence of R / : duration := duration(R /)
duration 
R1
P1
duration = 2
R1
P2
duration = 5

## Slide 44: Requirement SETS
Requirements can be grouped into sets of requirements
Boolean operators can be applied to all elements of a set:
  Unary operators:
  Binary operators:
S := { R1, R2, …, Rn }
ᴧ S := R1 ᴧ R2 … ᴧ Rn
op S := { op R1, op R2, …, op Rn }
ᴠ S := R1 ᴠ R2 … ᴠ Rn
 S := R1  R2 …  Rn
 S := R1  R2 …  Rn
¬S := { ¬R1, ¬R2, …, ¬Rn }
op S := R1 op R2 … op Rn

## Slide 45: Requirement sets
In general, requirements are requirement sets because they are in general associated with multiple time period. It is therefore also possible to associate multiple requirements with time periods and with multiple time periods.
The multiple time period associated with R = ϕ{P1, P2, …, Pn } is denoted R
Conditions associated with a multiple time period
Multiple condition associated with a time period
Multiple condition associated with a multiple time period
R = ϕ{P1, P2, …, Pn } := { ϕP1, ϕP2, …, ϕPn }
R = { ϕ1, ϕ2, …, ϕp }{ P1, P2, …, Pn }
:= { ϕ1{P1, P2, …, Pn }, ϕ2{ P1, P2, …, Pn }, …, ϕp{ P1, P2, …, Pn }}
= { ϕiPj, 1  i  p, 1  j  n }
= {{ ϕ1, ϕ2, …, ϕp }P1 }, {{ ϕ1, ϕ2, …, ϕp }P2 }, …, {{ ϕ1, ϕ2, …, ϕp }Pn }}
R = { ϕ1, ϕ2, …, ϕp }P := { ϕ1P, ϕ2P, …, ϕpP }
R := { P1, P2, …, Pn }

## Slide 46: Requirement Satisfaction over MULTIPLE time periods
The satisfaction of R = ϕ{ P1, P2, …, Pn } is
P╞ ϕ := ᴧ { P1╞ ϕ, P2╞ ϕ, … Pn╞ ϕ }
The satisfaction of R = { ϕ1, ϕ2, …, ϕp }{ P1, P2, …, Pn } is therefore
The satisfaction of R = { ϕ1, ϕ2, …, ϕp }P is
P╞ ϕ := ᴧ { P╞ ϕ1, P╞ ϕ2, … P╞ ϕn }
P╞ ϕ = ᴧ { Pj╞ ϕi, 1  i  p, 1  j  n }

## Slide 47: Definition non-overlapping multiple time periods
A non-overlapping multiple time period contains no overlapping time periods.
A non-overlapping multiple time period P is a multiple time period such that
P = (([ | ]) R, ¬R ([ | ]))
where R is a Boolean.
R
R
R
¬R
¬R
¬R

## Slide 48: Definition of Master time periods
E1
E1
E2
M
P1
P2
E2
R
R
A master time period M is a time period or a non-overlapping multiple time period that truncates time periods or multiple time periods P. The result of the truncation is a time period if M and P are time periods, or a multiple time period denoted M  P otherwise .
If M = (([ | ]) R, ¬R ([ | ])) and P = [ E1, E2 ], then
M  P := [ (R ᴧ E1), (¬R ᴠ E2) ]
If P = P1 // P2 // … // Pn, then
M  P := M  P1 // M  P2 // … // M  Pn

## Slide 49: ETL simulation: start and end of simulation time
ETL formula are independent of simulation time window: ETL time spans from to .
Simulation time window spans from t0 to tf.
The user must ensure that all events to be verified occur between t0 and tf, excluding t0 and tf. This can be done by encapsulating all events in a single master time period, that defines the beginning and the end of the test-case.
Before the beginning of the master time period, all requirements are evaluated to undefined: testing has not started. After the end of the master time period, all requirements are evaluated to true or false. If some requirements are still undefined or undecided, that means that not all events are within the master time period and testing is incomplete.
t0
tf
Test starts
Test ends
undefined
true or false
undefined, undecided, true or false

## Slide 50: Definition of domains
A domain is a finite or infinite set of entities of the same kind.
List of domains:
  : positive integers
  : positive or negative integers
  : complex numbers
  : Booleans
  : character strings
  : operators
  : requirements.  
  : time periods
  : discrete clocks
  : events
  : class C

## Slide 51: Definition of operators
An operator is a function between two domains and (that can be equal or not)
Domains and can be composed of multiple domains:
  = 1  2  …  n
  = 1 2  …  n
A unary operator on domain is a function
A binary operator on domain is a function
f : 
f : 
f :  

## Slide 52: Definition of Templates
Templates are operators on requirements taking Booleans as values.
Example: mission change. If requirement R1 fails, then requirement R2 should be satisfied at most 1h after R1 fails.
If mission change fails, then switch to R3
Example: if assumption A1 is verified then R1 should be satisfied, else R2 should be satisfied
missionChange (R1, R2) := ¬R1  R2 [R1, R1 + 1*h]
missionChange (missionChange (R1, R2), R3)
rule (A1, R1, R2) := (A1  R1) ᴧ (¬A1  R2)
t: 1  2  …  n 

## Slide 53: Definition of categories
Categories are operators on operators. They are introduced to handle the computation of operator a(R) in
A category is defined as an operation on a domain of operators
Example:
Example:
val(R) := a(ϕ) dϕ with R = ϕP

ϕ P
( )  ( )
o  C(o)
C(>) = >, C() = , C(<) = , C() = >, C() = >, C() = >
(  ) = { >, , <, , ,  }
(  ) = { true, false, undecided, undefined }
C(true) = false, C(false) = false,
C(undecided) = false, C(undefined) = false
ϕ := count (E, P)  2
a(ϕ) := count (E, P) C() 2 = ¬ϕ

## Slide 54: Definition of sets
A set S is a finite collection of n elements ai from the same domain :
There are no duplicates in a set.
If set S1 and set S2 have the same elements, they are equal even if their elements are listed in different orders.
S := { a1, a2, … an, ai  , 1  i  n }

## Slide 55: Operations on sets
If f is a unary operator defined on domain , and if A is a set of elements of then
If f is a binary operator defined on domain , and if A is a set of elements of then
Examples
f (A) := { f (ai), ai  A }
f (A) := f ( … f (f (a1, a2), a3), …, an), ai 
A := { R1, R2, …, Rn }
ᴧ A := R1 ᴧ R2 … ᴧ Rn
¬A := { ¬R1, ¬R2, …, ¬Rn }
 A := R1  R2 …  Rn
A := R{ P1, P2, …, Pn } := { RP1, RP2, …, RPn }
val(A) := { val(RP1), val(RP2), …, val(RPn) }
ᴧ val(A) := val(RP1) ᴧ val(RP2) … ᴧ val(RPn

## Slide 56: Operations on sets
If f is a function defined on domain, if Ai is a set of elements of then
Example
If some of the arguments of f have scalar values ai instead of set values Ai, then
where the scalar values are replaced by sets of single values
Example
f (A1, A2, …, An) := { f (a1j, a2j, …, aij, …, anj), aij  Ai }
R = f({ ϕ1, ϕ2, …, ϕp }, { P1, P2, …, Pn }) := { ϕ1, ϕ2, …, ϕp }{ P1, P2, …, Pn }
:= { ϕiPj, 1  i  p, 1  j  n }
f (A1, a2, … ap, … An) := f (A1, { a2 }, … { ap }, … An)
f(R, { P1, P2, …, Pn } ):= R{ P1, P2, …, Pn }
:= f(R, { P1, P2, …, Pn })
:= { f(R, P1), f(R, P2), … , f(R, Pn) }
:= { RP1, RP2, … , RPn }

## Slide 57: Operations on sets
Example of the evaluation of requirements
A := f(R, { P1, P2, …, Pn } ):= R{ P1, P2, …, Pn }
:= f(R, { P1, P2, …, Pn })
:= { f(R, P1), f(R, P2), … , f(R, Pn) }
:= { RP1, RP2, … , RPn }
val(A) := { val(RP1), val(RP2), …, val(RPn) }
ᴧ val(A) := val(RP1) ᴧ val(RP2) … ᴧ val(RPn

## Slide 58: Operations on sets
Remark:
  If f is a binary operator on domain , and if A is a set of elements of then
  Hence f (A) is a scalar value in.
  If f a function on domain , and if A is a set of elements of then
  Hence f (A, A) is a set value in
Example:
   { a1, a2, … , an } := a1  a2  …  an
  { a1, a2, … , an }  { a1, a2, … , an } := { ai  aj , 1  i  n, 1  j  n }
f (A) := f ( … f (f (a1, a2), a3), …, an), ai 
f (A, A) := { f (ai, aj) ai  A, aj  A, }

## Slide 59: Special sets
Special sets are sets with special operators:
  Sets of requirements
  Clocks: sets of events
  Multiple time periods: sets of time periods
  Sets of objects

## Slide 60: Preliminary Definition of Objects
An object O = { att1:, …, attn:n.} is a set of attributes where each attribute atti is defined as a function of time that takes its values in a domain .
Two objects O1 and O2 belong to the same class if they have the same attributes. They are not considered to be equal because at the same instant in time, their attributes can have different values.
Therefore:
  Two objects O1 and O2 of the same class only differ in the values of their attributes.
  A class is the domain of all objects having the same attributes.
Notation:
  Attribute atti of object O is denoted O.atti
  Object O belongs to class is denoted O . It is called then an instance of .
atti:  
where  is a clock (continuous or discrete):  = or  

## Slide 61: Preliminary definition of classes
A class is a domain of objects.
A class = { att1:, …, attn:n.} is a set of attributes where each attribute atti defines the domain of the values of the corresponding attribute atti of the instances of
A class ’ extends another class if all attributes of ’ are included in .
Notation:
  Attribute atti of class is denoted .atti
  Class ’ extends class is denoted ’  .
  The extension of class to class ’ is denoted ’ = + { att’1:, …, att’p:p.} , where att’1, …, att’p are the additional attributes.
A class ’ can extends several classes. This is denoted ’  1 + … + n. Then
’ = 1 + … + n+ { att’1:, …, att’p:p.}
Each attribute features only once in ’ (duplicates are removed).

## Slide 62: Examples of objects
Example: class Pump
  Pump := { char:, eff:, state:
  The first attribute contains the value of the pump characteristic
  The second attribute contains the value of the pump efficiency
  The third attributes tells whether the pump is started or not
Example: class CoolingSystem:
  oolingSystem := { Pump1:, Pump2:, Pump3:, state:
  Each of the first 3 attributes contain 1 object of class .
  The fourth attributes tells whether the cooling system is started or not.

## Slide 63: Operations on sets of objects
Set filter: S(cond ) := { Oi, cond(Oi.attj) = true } cond: condition
Example: all pumps that are started and close to their nominal regime
  Pump := { char:, eff:, state:
  Pumps := { P1, P2, P3, P4, Pi  Pump }
  PumpsStarted := Pumps(.state = true  .eff > 0.90)

## Slide 64: Domain extension
Existing domains can be extended to create new domains. For instance, can be extended to define the domain of physical quantities.
If domain extends domain , then all operations on can be applied on , unless specified otherwise (e.g., it is not possible to add or multiply temperatures).
Notation: domain extends domain is denoted 
If domain extends domain , then = var: + { att1:1, …, attn:n }, where att1 … attn are fixed attributes (i.e. that do not depend on time) and var denotes a variable of (that can depend on time).Therefore, is obtained by assigning fixed attributes to variables of .
A variable of z’  is obtained from a variable z  by providing fixed values to att1 … attn: z’ = z(att1=val1, …, attn=valn ).

## Slide 65: Domain extension
Example: defining the domain of physical quantities
= quantity: + { SIunit:, displayUnit:rate:, offset: }
Siunit: SI unit
displayUnit: display unit
rate and offset: converting display units to SI units:
  quantity (SI units) = rate  quantity (display units) + offset
The domain of pressures P expressed in Pa can be derived from by providing values to the attributes of : P_Pa = (SIunit=Pa, displayUnit=Pa, rate=1, offset=0).
The domain of pressures P expressed in bar can be derived from by providing values to the attributes of : P_bar = (SIunit=Pa, displayUnit=bar, rate=105, offset=0).
The domain of pressures P expressed in mbar can be derived from by providing values to the attributes of : P_mbar = (SIunit=Pa, displayUnit=bar, rate=102, offset=0).
Then, a = 2 bar can be expressed by a  P_bar with a = 2, or by a  P_mbar with a = 2000, or by a  P_Pa with a = 2 105.

## Slide 66: Language elements

## Slide 67: Summary of language types
Events
Requirement
Boolean
Events
evaluate
Boolean
Periods
Periods
Boolean
Boolean2 (true, false)
Boolean3 (true, false, undecided)
Boolean3 (true, false, undefined)
Boolean4 (true, false, undecided, undefined)
Classical Boolean
Classical Boolean with uncertainties
Classical Boolean trimmed by time period
Result of requirement evaluation

## Slide 68: 3- valued Booleans
Boolean3 (true, false, undecided)
Classical Boolean with uncertainties
true
false
undecided
uncertainty
Whether an operating point belongs to an operating domain

## Slide 69: Language types
A type corresponds to a domain.
  Boolean :=
  Category := (application on operators)
  Class C :=
  Clock :=
  Event :=
  Events :=
  Integer :=
  Operator := (operator )
  Period :=
  Periods := 2 (power set of )
  Real :=
  Requirement :=
  Requirements := 2 (power set of )
  Set := { A1, … An, Ai  }
  String :=
  Template :=

## Slide 70: CRML special values and characters
Special characters
  (
  )
  [
  ]
  {
  }
  ,
  .
  ;
Special values
  false
  true
  undecided
  undefined

## Slide 71: CRML keywords
+ usual operators on Integer and Real (+, , *, /, mod, …)
Operators on operators
  associate
  Category
  Operator
  Template
  filter
  is
  master
  not
  on
  par
  periods
  pre
  proj
  tick
  trim
  start
  sum
  with
Operators
  =
  *
  
  +
  <
  <=
  >
  >=
  ==
  and
  at
  card
  condition
  duration
  end
Attributes on variables
  external
  fixed
  parameter
Operators on objects
  alias
  Class
  Element
  extends
  forbid
  of
  Set
  Type

## Slide 72: Type: Boolean
Types
  Boolean b
  Events E
Constructors
  Boolean: Boolean b is Boolean_expr
  Boolean: Boolean b is E := E)
Predefined values
  true
  false
  undecided
  undefined
Logical operators
  Conjunction: b1 and b2 := b1 ᴧ b2  Boolean
  Negation: not b := ¬b  Boolean

## Slide 73: Type: Boolean
Temporal operators
  Previous: pre b :=  b  Boolean
  Filter: b1 * b2 := b1 x b2  Boolean
  Difference: b1  b2 := b1  b2  Boolean
  Accumulation: b1 + b2 := b1 + b2  Boolean
  Trim: trim b on P := trim(b, P)  Boolean
  Sum: sum b :=  b  Boolean
  Duration: duration b on P := duration(b, P)  Real

## Slide 74: Type: requirement
Types
  Requirement R
  Boolean b
  Periods P
Constructor
  Requirement: Requirement R is b on P := bP
Logical operators
  Condition: condition R := R  Boolean
  Conjunction: R1 and R2 := val(R1) ᴧ val(R2)  Boolean
  Negation: not R := ¬val(R)  Boolean
Temporal operators
  Periods: periods R := R  Periods

## Slide 75: Type: requirements (set of requirements)
Types
  Requirement R
  Requirements S
Constructors
  Requirements: Requirements S is { R1, R2, R3, R4 } := { R1, R2, R3, R4 }
  Requirements: Requirements S is R1 with R2 := { R1, R2 }
  Requirements: Requirements S is S1 with R := S  { R }
  Requirements: Requirements S is R with S1 := { R }  S
  Requirements: Requirements S is S1 with S2 := S1  S2
Logical operators
  Conjunction: and S := ᴧ S  Boolean
  Negation: not S := ¬S  Requirements

## Slide 76: Type: Event
Types
  Boolean b
  Event E
  Clock C
  Real d
  Integer n
Constructor
  Event: Event E is b := b (first occurrence of b becoming true)
Temporal operators
  Projection: E proj C := E/C  Event
  Projection: E proj(d) C := E/dC  Event
  Delay: E + d := E + d  Event
  Delay: E proj C + n := E/C + n  Event
  Elapsed time: E1  E2 := E1  E2  Real
  Elapsed time: E1 proj C  E2 proj C := E1/C  E2/C  Integer

## Slide 77: Type: Event
Temporal operators
  Before: E1 <= E2 := E1  E2  Boolean
  After: E1 >= E2 := E1  E2  Boolean
  Strictly before: E1 < E2 := E1  E2  Boolean
  Strictly after: E1 > E2 := E1  E2  Boolean
  Equality: (b1 == b2) at E := (b1 = b2)E  Boolean
Logical operators
  Union: E1 or E2 := E1 ᴠ E2  Clock

## Slide 78: Type: Clock or EVENTS (set of events)
Types
  Boolean b
  Clock C
  Real d
  Integer n
  Event E
Constructor
  Clock: Clock C is b := C(b)
Temporal operators
  Delay: C + d := C + d  Clock
  Projection: C1 proj C2 := C1/C2  Clock
  Tick filter: C filter Boolean_expr (tick) := C(cond )  Clock
Events is synonymous to Clock

## Slide 79: Type: Clock or events (set of events)
Temporal operators
  Union: C1 or C2 := C1 ᴠ C2  Clock
  Union: C or E := C ᴠ E  Clock
  Union: E or C := E ᴠ C  Clock
Set operator
  Card: card C := card(C)  Integer

## Slide 80: Type: period (single time period)
Types
  Period P
  Events E
Constructors
  Period: Period P is [ | ] E1, E2 [ | ] := ([ | ]) E1, E2 ([ | ])
Temporal operators
  Master period: P1 master P2 := P1  P2  Period
  Opening event: P start  Event
  Closing event P end  Event

## Slide 81: Type: periods (Multiple Time period)
Types
  Period P
  Periods M
  Events E
  Real d
Constructors
  Periods: Periods M is P1 par P2 := P1 // P2
  Periods: Periods M is [ | ] E1, E2 [ | ] := (([ | ]) E1, E2 ([ | ]) )
  Periods: Periods M is [ | ] E, d [ | ] := (([ | ]) E, d ([ | ]) )
Temporal operators
  Master period: M master P := M  P  Periods
  Master period: P master M := P  M  Periods
  Master period: M1 master M2 := M1  M2  Periods

## Slide 82: Type: operator
Types
  any_type E
  String s
Constructor
  Operator: Operator [ return_type_E ] s1 type_E1 E1 s2 type_E2 E2 s3 …. sn-1 type_En En sn = expr (E1, …, En) that evaluates to type_E
Example: counting events generated by a Boolean inside a time period
  Operator [ Clock ] Clock C inside Period P = C filter (tick >= P start) and (tick <= P end)
  Operator [ Integer ] count Requirement R becomes true inside Period P = card Clock R inside P
  Requirement R
  Period P
  Integer n = count R becomes true inside P

## Slide 83: Type: Template
Types
  Requirement R
  String s
Constructor
  Template: Template s1 R1 s2 R2 s3 …. sn-1 Rn sn = Operator [ Boolean ] s1 Requirement R1 s2 Requirement R2 s3 …. sn-1 Requirement Rn sn
Example: logical disjunction
  Template R1 or R2 = not (not R1 and not R2)
  Requirement R1
  Requirement R1
  Requirement R = R1 or R2

## Slide 84: Type: category
Types
  Operator O
  Category C
  String s
Constructor
  Category: Category s = { (O11, O12), (O21, O22), … (On1, On2) }
Operators
  Associate: associate C with O  -

## Slide 85: Meta-type: type
Types
  Type T
Constructor
  Parametrized type:
  Type:
Type T2 extends T1 t {
alias alias_name;
parameter type_par_1 par_1;
parameter type_par_m par_m;
type_var_1 var_1 is expr (t, par_1, …, par_n);
type_var_n var_n is expr (t, par_1, …, par_n);
forbid op_1, op_2, …, op_n;
} := T1 + { par_1:type_par_1, par_2:type_par_2 …, par_n:type_par_n }
Type T3 extends T2 (par_1=val_1, par_2=val_2 …, par_n=val_n) {
forbid op_1, op_2, …, op_n;
}

## Slide 86: Meta-type: type
Types
  Type T
Constructor
  Variable: T2 var(par_1=value_1, …, par_m=value_m)  T2
  Variable: T1 var(par_1=value_1, …, par_m=value_m) alias_name  T2

## Slide 87: Meta-Type: Class of objects
Types
  Class C;
Constructor
  Class:
Operators
  Extends: C’ extends C := C’  C  C’
Class C is {
parameter type_par_1 par_1;
parameter type_par_2 par_2;
.
parameter type_par_m par_m;
external type_var_1 var_1;
type_var_2 var_2;
.
type_var_n var_n;
} := { var_1:type_var_1, var_2:type_var_2 …, var_n:type_var_n }

## Slide 88: Type: object
Types
  Class C
Constructor
  Object: C O (par_1=val_1, par_2=val_2, …, par_m=val_m)
Operators
  Get attribute: O.var_i  type_var_i

## Slide 89: Type: set of objects
Types
  Class C
  C O;
  Set S of C
Constructor
  Set: Set S of C is { O1, O2, O3 } := { O1, O2, O3 }
  Empty set: Set S of C is { }
Operators
  Union: S1 with S2 := S1  S2  Set of C
  Card: card S := card(S)  Integer
  Filter: S filter Boolean_expr (element) := S(cond )  Set of C

## Slide 90: CRML Library of types

## Slide 91: Physical quantities
Type Quantity defines the domain of physical quantities. The variable is referred to as “quantity”, which holds the value used for model calculations. The variable has the following attributes:
  displayUnit: unit used by the user
  Siunit: SI unit of the quantity
  ratio and offset: coefficients to translate the value provided by the user into the value used for the model calculations, i.e. translating display units into SI units according to the formula: display unit = rate  SI unit + offset
Type Quantity extends Real quantity {
  parameter String displayUnit;
  parameter String SIunit;
  parameter Real ratio;
  parameter Real offset;
  Real quantity_displayUnit = rate  quantity + offset;
  }

## Slide 92: Physical quantities: Pressure
Type AbsolutePressure extends Quantity (SIunit=“Pa“) { forbid +, *; }
Type AbsolutePressure_Pa extends AbsolutePressure (displayUnit=“Pa“, ratio=1, offset=0) { alias “Pa”; }
Type AbsolutePressure_bar extends AbsolutePressure (displayUnit=“bar“, ratio=1.e-5, offset=0) { alias “bar”; }
Type AbsolutePressure_mbar extends AbsolutePressure (displayUnit=“mbar“, ratio=1.e-2, offset=0) { alias “mbar”; }
Example: to declare a variable that represents an absolute pressure of 2 bar:
  AbsolutePressure var is 2 bar
  Meaning of the declaration: var belongs to the subtype of AbsolutePressure that corresponds to alias “bar” which is AbsolutePressure_bar. The declaration is equivalent to:
    AbsolutePressure_bar var is 2
  For all declarations, the value of the variable used for computation is its value in SI units.

## Slide 93: Physical quantities: Pressure
Type PressureDifference extends Quantity (SIunit=“Pa“) { forbid -, *; }
Type PressureDifference_Pa extends PressureDifference (displayUnit=“Pa“, ratio=1, offset=0) { alias “Pa”; }
Type PressureDifference_bar extends PressureDifference (displayUnit=“bar“, ratio=1.e-5, offset=0) { alias “bar”; }
Type PressureDifference_mbar extends PressureDifference (displayUnit=“mbar“, ratio=1.e-2, offset=0) { alias “mbar”; }

## Slide 94: CRML Library of ETL operators

## Slide 95: Logical operators
Logical disjunction
  Template R1 or R2 = not (not R1 and not R2)
Exclusive logical disjunction
  Template R1 xor R2 = (R1 or R2) and not (R1 and R2)
Logical inference
  Template R1 implies R2 = not R1 or R2

## Slide 96: operators on clocks and events
Filter clock ticks inside a time period
  Operator [ Clock ] Clock C inside Period P = C ticks (tick >= P start) and (tick <= P end)
Count the occurrences of events inside a time period
  Operator [ Integer ] count Events E inside Period P = card E inside P

## Slide 97: operators on events
Events generated when a Boolean becomes true
  Operator [ Events ] Boolean b becomes true = Events b
Events generated when a Boolean becomes false
  Operator [ Events ] Boolean b becomes false = not b becomes true
Events generated when a Boolean becomes true inside a time period
  Operator [ Events ] Boolean b becomes true inside Period P = (b becomes true) inside P
Events generated when a Boolean becomes false inside a time period
  Operator [ Events ] Boolean b becomes false inside Period P = (b becomes false) inside P

## Slide 98: operators on events
Events generated when a requirement becomes true
  Operator [ Events ] Requirement R becomes true = (evaluate R) becomes true
Events generated when a requirement becomes false
  Operator [ Events ] Requirement R becomes false = not R becomes true
Events generated when a requirement becomes true inside a time period
  Operator [ Events ] Requirement R becomes true inside Period P = (R becomes true) inside P
Events generated when a requirement becomes false inside a time period
  Operator [ Events ] Requirement R becomes false inside Period P = (R becomes false) inside P

## Slide 99: CRML Library of ETL operators for the evaluation of requirements

## Slide 100: Categories for the evaluation of requirements
Category increasing = { (>, >), (>=, >=), (<, >=), (<=, >), (==, >), (<>, >) }
  associate increasing with decide
Category decreasing = { (>, >), (>=, >=), (<, <), (<=, <=), (==, <), (<>, <) }
  associate decreasing with decide
Category varying = { (true, false), (false, false), (undecided, false), (undefined, false) }
  associate varying with decide
If category cat is associated with decide:
  then in operator decide, the operators cat op are substituted by cat op
    Example: cat < is replaced by >= for cat = increasing
If category cat is associated with no other operators:
  then in all other operators, cat op are substituted by op
    Example: cat < is replaced by < for any cat
This is needed to signal as early as possible that a requirement is satisfied (and not only at the end of the time period).

## Slide 101: Operators for the evaluation of requirements
Differential operator
  Operator [ Boolean ] diff Boolean phi = phi  pre phi
Logical integral operator
  Operator [ Boolean ] integrate Boolean phi wrt Boolean tau over Period P = sum (phi*diff (trim tau on P))
Decision operator
  Operator [ Boolean ] decide Boolean phi over Period P = Boolean ((Events phi) or (P end))
Evaluation operator on a single time period
  Operator [ Boolean ] evaluate Boolean phi over Period P = integrate (decide phi over P) wrt phi over P
Evaluation operator
  Operator [ Boolean ] evaluate Requirement R = and (evaluate condition R over periods R)
Satisfaction operator when an event E occurs
  Operator [ Boolean ] sat Requirement R when Event E = (evaluate R == true) at E
ϕ() d := ϕ() x d

 P

P
val(ϕP) := a(ϕ) d ϕ

ϕP
d ϕ := ϕ   ϕ
val(ϕP) = ᴧ val(ϕ{Pi, 1  i  n }) = ᴧ { val(ϕPi), 1  i  n }
a(ϕ)

## Slide 102: CRML Library of FORM-L operators

## Slide 103: Time periods
From events occur
  Operator [ Periods ] from Events E = Periods [ E, Events false ]
After events occur
  Operator [ Periods ] after Events E = Periods ] E, Events false ]
Before events occur
  Operator [ Periods ] before Events E = Periods [ Events false, E [
Until events occur
  Operator [ Periods ] until Events E = Periods [ Events false, E ]
While a Boolean is true
  Operator [ Periods ] during Boolean b = Periods [ Events b, Events not b ]

## Slide 104: Time periods
After events occur and before events occur
  Operator [ Periods ] after Events E1 before Events E2 = Periods ] E1, E2 [
After events occur and until events occur
  Operator [ Periods ] after Events E1 until Events E2 = Periods ] E1, E2 ]
After events occur and for an elapsed time
  Operator [ Periods ] after Events E for Real d = Periods ] E, d ]
After events occur and within an elapsed time
  Operator [ Periods ] after Events E within Real d = Periods ] E, d [

## Slide 105: Time periods
From events occur and before events occur
  Operator [ Periods ] from Events E1 before Events E2 = Periods [ E1, E2 [
From events occur and until events occur
  Operator [ Periods ] from Events E1 until Events E2 = Periods [ E1, E2 ]
From events occur and for an elapsed time
  Operator [ Periods ] from Events E for Real d = Periods [ E, d ]
From events occur and within an elapsed time
  Operator [ Periods ] from Events E within Real d = Periods [ E, d [

## Slide 106: Time periods
When events occur
  Operator [ Periods ] when Events E = Periods [ E, E ]

## Slide 107: requirements
Checking a requirement
  Operator [ Boolean ] Periods P check Boolean b = evaluate Requirement b on P
Checking that a requirement is satisfied at the end of a time period
  Operator [ Boolean ] Periods P check at end Boolean b = P varying check b

## Slide 108: requirements
Checking that the number of event occurrences at the end of a time period is lower or higher than a threshold
  Operator [ Boolean ] Periods P check count Events E < fixed Integer n = P check ((count E inside P) increasing < n)
  Operator [ Boolean ] Periods P check count Events E <= fixed Integer n = P check ((count E inside P) increasing <= n)
  Operator [ Boolean ] Periods P check count Events E > fixed Integer n = P check ((count E inside P) increasing > n)
  Operator [ Boolean ] Periods P check count Events E >= fixed Integer n = P check ((count E inside P) increasing >= n)
  Operator [ Boolean ] Periods P check count Events E == fixed Integer n = P check ((count E inside P) increasing == n)
Ensuring that a requirement is satisfied all along a time period
  Operator [ Boolean ] Periods P ensure Boolean b = P check count (not b becomes true) == 0

## Slide 109: requirements
Checking that the duration of a condition at the end of a time period is lower or higher than a threshold
  Operator [ Boolean ] Periods P check duration Boolean b < fixed Real d = P check ((duration b on P) increasing < d)
  Operator [ Boolean ] Periods P check duration Boolean b <= fixed Real d = P check ((duration b on P) increasing <= d)
  Operator [ Boolean ] Periods P check duration Boolean b > fixed Real d = P check ((duration b on P) increasing > d)
  Operator [ Boolean ] Periods P check duration Boolean b >= fixed Real d = P check ((duration b on P) increasing >= d)

## Slide 110: References
Bouskela D., Nguyen T. and Jardin A. (2017), “Toward a Rigorous Approach for Verifying Cyber-Physical Systems Against Requirements,” Canadian J. of Electrical and Computer Engineering, Vol. 40-2, pp. 66-73.
Bouskela D. and Jardin (2018), “ETL: A New Temporal Language for the Verification of Cyber-Physical Systems,” 2018 Annual IEEE International Systems Conference (SysCon).
Bouskela D., Falcone A., Garro A., Jardin A., Otter M., Nguyen T., and Tundis A. (2020), “Formal Requirements Modeling for Cyber-Physical Systems Engineering,” to be published.

## Slide 111: Thank you for your attention